## Slide 1: Representations
Mobile Robotics 2023

## Slide 2: Brief Review
Space-fixed (Extrinsic Rotation) vs body-fixed frame (Intrinsic Rotation)
Euler angles in space-fixed frame vs body-fixed frame

## Slide 4: Today
Additional disadvantages with Euler Angles
  Gimbal Lock
Quaternions
  Introduction
  Quaternion Algebra
  Rotation in Quaternions
  Rotation Matrix ⇔ Quaternions
  Axis Angles ⇔ Quaternions
  Interpolation

## Slide 5: Gimbal Lock - Computational Perspective

## Slide 6: Gimbal Lock
Now, rotate the rigid body about the z-axis of space-fixed frame

## Slide 7: Gimbal Lock - Computation Perspective
Cannot reach all the configurations once it gets locked
Creates problems in conversions, interpolation, derivatives, …etc.

## Slide 8: Summary of problems with Euler angles
Calculating inverse in ABA convention is straight forward
  However, ABC convention is not trivial
Composition is non-trivial and hence the interpolation is non-trivial
Not continuous at 0 and 2*pi
Gimbal Lock creates numerical instability while dealing with problems such as inter-conversion, derivatives, and interpolation

## Slide 9: Quaternions
Complex numbers in 2D space can represent rotations
  Can we extend this to 3D space?
Properties of Quaternions
  Addition
  Multiplication
  Conjugate
  Norm
  Inverse

## Slide 10: Representing Rotations using Quaternions
Rotation encoded as a quaternion
Point as a quaternion
Performing rotations in quaternion space

## Slide 11: More on Quaternions
Comparison to Axis Angles
What about the problems faced with Euler representation?
  Geodesic Interpolation is possible in Quaternion space using SLERP
    Geodesic interpolation for any other representation would require us to first convert to matrix space and then apply axis-angle approach